Yagi Analysis Ver. 3.54
        
       INTRODUCTION
        
       Yagi Analysis is a Yagi calculating program that has been on the
       market for a couple of years now.
       Ver 3.0 has been  restyled and now includes both drop-
       down and pop-up menus.
       Mouse support is also included.
       Calculations can be based on one or up to 10 frequencies.
       When calculating an antenna using several frequencies a comparison
       of radiation pattern and flow for the various frequencies is made.
       Yagi Analysis also calculates the antenna's efficiency.
       With Ver 3.52  you can calculate G/T and stack up to 44 element Yagis.
       You can  save your antennafiles in NEC format, and if you have NEC 
       you can compare your antenna pattern with the pattern calculated with
       NEC.
       In ver 3.52 the Gain  has been reduced  with the loss.
       Some improvements have been made in Ver 3.52 with the end effect 
       calculations  on large element diameters.


       RELIABILITY
        
       Yagi Analysis is of the same class as NEC for normal Yagi
       antennas.
       A comparison has shown that results from Yagi analysis have agreed
       with NEC.
       Some improvements have been made in Ver 3.52 with the end effect 
       calculations  on large element diameters.
       On the other hand, these results have not agreed with other
       antenna programs such as Yagimax, MN, YO and other Mininec based
       programs. This is because these programs do not agree very well
       with NEC, even if this claim is sometimes made.
       Yagi Analysis is 5-100 times faster than NEC depending on antenna
       size.
       The time gain increases with the size of the antenna.
        
        
       INSTALLATION
        
       To be able to use the Yagi Analysis program an IBM PC or
       compatible computer is needed with more than 500K of free memory.
       The computer must also be equipped with a hard disk.
       The program supports CGA, EGA and HGC.
       An Epson compatible printer is needed to print out the screen
       graphics.
       Using a maths co-processor is recommended to increase speed of
       calculation.
       If CGA is being used, GRAFTABL and GRAPHICS must be loaded before
       running Yagi Analysis. The programs can be found on your DOS disk
       and are used when printing screen graphics.
        
        
       1. Insert program disk  into drive A: and
       Type A:
       Press <RETURN>
       Type INSTALL
       Press <RETURN>
        

       This starts the Install program. You must now enter  drive and 
       path where you want to have Yagi Analysis .
       Default is:   C:\YAGI
       You must also enter Drive and Path for NEC out and data files.
       Default is:   C:\NEC2   and   C:\NEC2\DATA
       Press F9 to continue.

       Now you can enter the type of graphics card you are using. 
       You can choose between EGA, CGA and Hercules.
       After making your choice you must press < RETURN > 
       Install will now copy Yagi Analysis to the harddisk and  ask you 
       for the serial number that is on the disk label.
        
       After typing the serial number press <RETURN> and you will then be
       asked for your name, signal or the name of the firm that owns the
       program.
       It is important that you initiate the disk properly to enable you
       to upgrade the program at reduced cost as new versions are
       released.
       Press <RETURN>.
       The program has now been initiated and is ready to use.
        
        
       Starting YAGI ANALYSIS
        
       Type: YAGI
       Press <RETURN>
       The program will now start and an information text will appear on
       the screen, showing the program name and serial number.
       Press <RETURN> to continue.
       
        
        
       PROGRAM DESCRIPTION
        
       Menus
       The program has drop-down and pop-up menus. It also supports a
       Microsoft mouse.
       At the top of the screen is the main menu:
        
       FILES  EDIT  RUN  RESULTS  OPTIONS
        
       The current date is also shown at the top of the screen.
       If an antenna file has been loaded the file name will be displayed
       between the menu and current date.
       At the bottom of the screen the program name, version number and
       your name will be displayed.
        
       You can access the drop-down menu by pressing <ALT> and the letter
       that is highlighted when you press <ALT>.
       If you have a mouse the menus can be accessed by clicking on the
       menu alternative you want.
        
       After pulling down a menu the options can be selected in three
       different ways.
       1. Each line of the menu has a letter that is highlighted in a
       different colour. By pressing the corresponding letter 
       on yhe keyboard the option will be activated.
        
       2. An option can also be selected by pressing the UP and DOWN
       arrows on the keyboard and pressing <RETURN>.
        
       3. If you are using a mouse just position the pointer on the
       option you want and click the mouse button.
       To exit from an option press <ESC> or click on the <CANCEL>
       option.

       
       If you have changed some data or entered new data in a sub-menu
       this must be confirmed by moving the cursor with the <TAB> key to
       <OK> and pressing <RETURN>.
       You can also use your mouse by clicking on <OK>.
       If you press <ESC> or click on <CANCEL> the data you have entered
       will be ignored.
       You can reach the Help text by pressing F1
        
        
       A SHORT DESCRIPTION OF THE MENUS.
        
       The first menu alternative is called Files and includes the
       following options or sub-menus:
       New
       Load
       Save
       Save Nec
       Print
       Plot
       Exit
        
       New is for entering new antenna data.
        
       Load is for retrieving previously entered antenna data.
        
       Save is for storing new data or an antenna calculation.

       Save Nec is for saving data in Nec format.
        
       Print is for printing out antenna data after calculation.
        
       Plot is for plotting the radiation pattern in polar form on an HP-
       7475 plotter.
        
       Exit is for exiting the program.
        
        
       EDIT menu
       This menu includes the following options or sub-menus:
       Elementdata
       Length of Taper
       Radii of Taper
       Frequency
       Director number
       Boom corr
        
       Elementdata is for entering and changing element position,
       spacing,lengths and radii.
        
       Length of Taper is for entering and changing length of element
       taper.
        
       Radii of Taper is for entering and changing radii of element taper
        
       Frequency is for changing the starting frequency, frequency
       interval and number of frequencies to be analysed.
        
       Director number is for changing the number of directors on an
       antenna.
        
       Boom corr is for correcting element lengths to compensate for the
       effect the boom has on the antenna.


       

       RUN menu
       This menu has only one option - "Run", and is used when making
       antenna calculations.
        
        
       RESULTS menu
       This menu is for viewing the results of a calculation and consists
       of the following sub-menus:
       Data
       Polar E-Pattern
       Polar H-Pattern
       Rectangular E-Pattern
       Rectangular H-Pattern
       Result-Graf
       Current-Graf
       Current-Phase
       Current
       Showing Noise Temperatue (G/T)
        
       Data shows a summary of the results of the calculation, e.g. Gain
       Imp, F/B etc.
        
       Polar E- and H-Pattern show the radiation pattern in polar form.
        
       Rectangular E- and H-Pattern show the radiation pattern in
       rectangular form.
        
       Result-Graf shows Gain, F/B and VSWR as a function of the
       frequency.
        
       Current-Graf shows the relative magnitude of the element currents
       in relation to the greatest magnitude.

       Current-Phase shows the element phases in a column chart 

       Current shows the element currents and their phase position and
       magnitude.

       Showing Noise Temperatue (G/T) shows the Noise Temperature and G/T
       computed . (See Options menu)
        
        
        
        
       OPTIONS menu
       This menu has the following options or sub-menus:
       Dimension unit
       Reflector Type
       Driver Type
       Element Pos
       Change Colors
       Wire Conductivity
       Ground/Stacking 
       Stacking
       Noise Temperatue (G/T)

       Dimension unit is for switching between millimetres, inches and
       wavelengths.
        
       Reflector Type is for switching the reflector configuration
       between single, double, triple and triangular.
        
       Driver Type is for switching between straight and folded dipole.

       
       Element pos is for switching the form in which element spacing
       will be entered.
        
       Change Colors is for switching color standard. The options are
       Color, Mono and LCD.
        
       Wire Conductivity is for changing the conductivity according to
       which material is used in the element. This is necessary in order 
       to calculate the correct efficiency.
        
       Ground/Stacking is for modelling  the Yagi over a prefectly-
       conducting groundplane, or stacking two Yagis.   
        
       Stacking is for entering stack spacing and number of antennas when
       stacking.

       Noise Temperature is for calculating how much Noise the Antenna
       will pickup.

       A DETAILED DECSCRIPTION OF THE MENUS.
        
       NEW
       To analyse a new antenna its data must be entered. To do this the
       NEW option is used.
       Activate the option by pressing <ALT> + F + N. The menu for
       entering new antenna data will now appear.
       A number of data fields and a box with default data will now be 
       displayed. The deafult data box contains Dimension, Refl.Type, 
       Driver Type and Element pos. You can change these data with the 
       F5 to F8 tangents.
       The first edit field is for the number of directors.
       Type a value and press <RETURN>.
       Next, you must enter the starting frequency. Type the frequency in
       MHz and press <RETURN>.
       You must now enter the spacing between each new frequency. Type
       the value in MHz and press <RETURN>.
       The number of frequencies to be calculated must now be entered.
       The highest value allowed is 10. Type a value and press <RETURN>.
       The cursor will now be at the STEP: field.
       If you have chosen or wish to choose element tapering the number of
       tapers per element must be entered here. If you have not chosen
       tapering just press <RETURN> and the cursor will move to <OK>.
       When you are satisfied with the data you have entered move the
       cursor to <OK> and press <RETURN> again to confirm that it is
       correct. If you want to change some data you can move to the data
       field you wish to change by using the arrow keys. Enter the
       correct value and using the <TAB> key move the cursor to <OK>
       again.
       Press <RETURN>.
       Depending on your choice of Tapering or not,( see Element Tapering)
       two different menus can appear.
       With Tapering element the Length of Taper menu will appear. In
       other case the Elementdata menu will appear.
        
        
       ELEMENT TAPERING
        
       With this option you can select to use element tapering
       (telescopic element) or mono-tapering.
       Select "Yes" by moving the cursor in the brackets with the
       <TAB> key or by clicking on it with the mouse.
       With the cursor in the brackets you can select or unselect Element
       Tapering by pressing the Spacebar.
       You can now move the cursor by pressing <TAB> or clicking with the
       mouse on the desired place.
       

       NOTE: Element tapering must be selected before entering new
       antenna data. Element tapering cannot be selected if data for a
       mono-tapered antenna has already been entered.
       When using element tapering Yagi Analysis will recalculate the
       elements to mono-tapering with an algorithm from W2PV. This
       algorithm converts the telescopic elements to normal non-tapering
       elements with the same internal impedance as the telescopic.
       When entering the element lengths start from the centre i.e. the
       antenna boom, and work towards the tip of the element.
        
        
        
       ELEMENTDATA MENU
        
       This menu is for entering the element position, lengths and radii.
       It consists of four editfields, four listboxes and five buttons.
       The leftmost listbox and editfield is named: EL_name, and
       contains the name of the elements.
       The other listboxes and editfields contain Element position or
       distance between elements, element lengths and element radii.
       The five buttons are <OK>, <CANCEL>, <INSERT>, >DELETE>, and
       <HELP>.
       You can activate these buttons by pressing F5-F1  or by clicking
       on a button with the mouse.
        
        
       EL_pos , EL_Distance
        
       There are two methods for entering the element position.
        
       1. Entering spacing between adjacent elements.
       This method is easier to edit if element spacing is changed.
        
       2. Entering the actual position of the element in relation to the
       reflector which is assumed to have position "0".
       This method is always used with element tapering.
       The desired method is chosen at the Options menu.
        
       The position of the first reflector Re1 is always "0".
        
       If more than one reflector is being used (see Options menu) use
       the <HELP> option to see how the data is to be entered. The <HELP>
       option is activated by pressing F1 or clicking on <HELP> if you
       have a mouse.
        
       Enter elementposition ("0" for the first reflector) and press
       <RETURN>. The cursor will move to the EL_LENGTH editfield .
       By pressing F10 you can lock the cursorto the El_pos editfield.
       If chosen method is EL_distance and two or more adjacent elements
       have the same spacing between each other, you only need to press
       <RETURN> and the previous spacing is copied to the current
       editfield.
        
        
       EL_Length
       This editfield is for entering the lengths of the elements.
       If two or more adjacent elements have the same length you only
       need to press <RETURN> and the previous value is copied to the
       current element.
       
       The length must be endpoint-to-endpoint and not 
       centre-to-endpoint as in some other programs.
       If a folded dipole is being used you must go to the Options menu
       and select Folded. You will then be asked to enter the dipole
       length and diameter.
        
       After pressing <RETURN> the cursor will move to the EL_Radii
       editfield.
       You can lock the cursor to the EL_length field by pressing F10.
        
        
       EL_Radii
       This editfield is for entering the elementRadii.
       Note that it is the radius and not the diameter that is entered.
       (See EL_Length for more information)
        
        
       <INSERT>
       Elements can be added by pressing F3 or clicking on <INSERT> if you
       have a mouse.
       To add an element, first mark the element in front of the place
       where the new element is to be added, and press F3.
       All data for the new element will be "0".
       Enter the new element data and press <RETURN>.
        
       <DELETE>
       Elements can be removed by clicking on <DELETE> or by pressing F2.
       To remove an element just mark the desired element and press F2.
        
       Elements can be marked by moving the marker line with the arrow key
       or by clicking on the desired element if you have a mouse.
        
       If you are satisfired with the data you have entered just press F5
       or click on <OK> if you have a mouse.
        
        
        
       LENGTH OF TAPER MENU
        
       If you have chosen Tapering element and pressed <OK> in the NEW
       menu, the Length of Taper menu will appear.
       This menu is for entering the Taper lengths of all elements.
       When entering the element lengths start from the centre i.e. the
       antenna boom, and work towards the tip of the element.
       If two or more adjacent tapers have the same length you only need
       to press <RETURN> and the previous value is copied to the current
       taper.
       You can move the cursor to a desired element tap with the arrow
       keys or by pressing the <TAB> key or by clicking on it if you have
       a mouse.
       If you are satisfied with the data you have entered just activate
       the <OK> button with the <TAB> key or (and) the arrow keys  and
       press <RETURN>.
       The menu named Radii of Taper will now appear.
        
        

       Radii of Taper

       This menu is for entering or changing element radii for tapering
       elements.
       You can enter the radii for the reflector driver and the first
       director only. The remaining directors are assumed to have the
       same radii as the first.
       The first data field for each element holds the radius of the
       element section nearest to the boom and so on.
       If all the elements have the same tapering radii you can speed up
       the procedure by pressing <RETURN> when the cursor is placed at
       the first data field of the second element. The previous elements
       radii will be copied to the data fields of the current element.
       Confirm the data with <OK> .
       The Elementdata menu will now appear and you can now enter the
       position of the elements. The Elementlengths and element radii
       that will appear in the elementdata menu is the monotaper
       calculated lengths and radii.(See Elementdata menu for more
       information).
        
        
        
       All the data have now been entered and you can select RUN to start
       calculating.
        
       Press <ALT> + R + <RETURN> and calculating will start.
       An information box with the word "Working" will now appear on the
       screen.
       When the calculations are ready the sub-menu Data will appear with
       a summary of the results.
        
        
        
        
       LOAD
        
       The Load option is for retrieving antenna files previously stored
       on floppy disk or hard disk.
       Press <ALT> + F and then "O". The menu for retrieving files will
       now be shown.
       All the accessible antenna files will be listed and you can select
       the antenna file you wish by using the arrow keys. Press <RETURN>
       and the antenna file will be loaded. You can also click with the 
       mouse on the antenna file you wish to load.
       When the antenna file has been loaded the sub-menu Data will
       appear showing a summary of the antenna data.
        
        
        
       SAVE
        
       To save an antenna file to disk select the Save option from the
       Files menu.
       The program will suggest a file name for the antenna. To accept
       this name just press <RETURN> and the file will be saved.
       If you want to give the file a different name press the arrow UP
       key and change the name. Then press <RETURN> twice.
       The file name may consist of up to 8 characters.
       If the file name you have chosen is not accepted or if it already
       exists an error message will be shown and you will be able to
       change the name.
        


       SAVE NEC

       You can now save the antenna files from Yagi Analysis in NEC format.
       If you have NEC you can  compute the antenna with NEC and then  
       use F6 in the pattern diagram to compare  results from Yagi 
       Analysis with NEC.


       PRINT
        
       The Print option can also be accessed from the Files menu and is
       for printing the antenna data after calculation.
        
        
       PLOT
        
       If you want to plot the radiation pattern on an HP-7475 plotter
       use the Plot option from the Files menu.
       After selecting plot from the menu you will be asked if you want
       to rotate the diagram 90 degrees. On certain plotters this
       operation is necessary for the diagram to be placed correctly on
       the paper.
       The following communications protocol is used:
       BAUDE RATE: 9600
       DATA BITS: 7
       STOP BITS: 2
       PARITY: EVEN
       CABLE: Standard plotter cable.
        
        
        
       EXIT
        
       If you want to exit Yagi Analysis select Exit from the Files menu.
        
        
        
       EDIT MENU
        
       Elementdata
       The first sub-menu under Edit is Elementdata
       This menu is for changing Position, length and radii for all
       elements .
       When Tapering element is chosen this menu only is for changing
       element position.
       (See elementdata menu for more information)
        
        
       Length of Taper
       This sub-menu is only shown when element taper is chosen, and
       is for changing the taper lengths of all elements.
       (See Length of taper above for more information)
        
       Radii of taper
       This sub-menu is only shown when element taper is chosen, and
       is for changing the taper Radii of all elements.
       (See Radii of taper above for more information)
        
        
        
       Frequency
       This menu is for changing start and step frequencies and the
       number of frequencies to be calculated.
       Enter the starting frequency in the first data field.
       Enter the frequency step in the second data field. This is the
       spacing between each frequency to be calculated.
       Enter the number of frequencies to be analysed in the last data
       field. The largest number allowed is 10.
        

        
       Director number
       If you want to lengthen or shorten an antenna select Director
       number from the Edit menu.
       The data field containing the current number will be shown. Enter
       the new value and press <RETURN> twice.
       If you increase the number of directors remember to also enter the
       new element lengths and positions or spacing.
        
        
       Boom corr
       This sub-menu is for compensating element lengths for the diameter
       of the antenna boom. The compensation will differ according to how
       the elements are mounted.
       Enter the diameter of the boom in the first data field. After
       pressing <RETURN> the compensation based on a diagram after
       measurement of DL6WU will be shown in the last data field.
       This compensation is applicable if the elements are mounted
       through the boom. If the current construction differs from this
       you can press <TAB> twice to access <Help>. Press <RETURN> and you
       will see a diagram that shows how boom compensation decreases as
       the distance between the elements and the centre of the boom
       increases. Select the mounting factor that is applicable to your
       element mounting and press <RETURN>.
       You will now be returned to the Boom corr menu. As the diameter of
       the boom was not confirmed before selecting <Help> this must be
       entered again.
       Enter the mounting factor in the second data field and confirm the
       data by pressing <TAB> until the cursor is on <OK> and press
       <RETURN>.
       The elements will now be lengthened by the boom corr factor and by
       selecting the Print option from the Files menu you will obtain a
       print-out of the new element lengths.
       If you want to analyse an existing antenna you must remove the
       boom compensation from the element lengths.
       Measure the element lengths and enter these in the Element length
       menu. Then select Boom corr and enter boom diameter and mounting
       factor. Now place a minus in front of the boom corr factor.
       The element lengths will now be decreased by boom corr and you can
       start analysing the antenna.
        
        
        
       RUN MENU
       To calculate an antenna after entering or changing the antenna
       data use RUN.
       The program will then check for faulty data and if everything is
       correct start to calculate. "Working" will be shown on the screen
       while calculating is in progress.
       When calculating is finished the sub-menu "Data" will appear
       showing a summary of the results.
       




       RESULTS MENU
       Use this menu to view the results of a calculation.
        
       Data
       This is the first sub-menu and shows a summary of the results.
        
       Polar E-pattern, H-pattern
       These options are for viewing the radiation pattern in polar form.
        
       Rectangular E-pattern, H-pattern
       These options are for viewing the radiation pattern in rectangular
       form.
        
       If you have calculated several frequencies when selecting polar or
       rectangular you will first see a sub-menu where you can select
       which frequency you want to view.
        
       Compare Nec
       If you have NEC and have computed your antenna with NEC,
       you can compare the radiation pattern from your antenna with the
       pattern calculated with NEC.

       Compare freq., ant.
       You can compare the radiation pattern from a different antenna or
       a different frequency (if more than one frequency has been
       calculated).
       By pressing F7 you can select another antenna and by pressing F8 
       another frequency.
       The patterns will be superimposed on each other for a direct
       comparison.
        
        
       Screen dump
       You can make a screen dump to a printer by pressing F9. If you are
       using CGA graphics you must press Prt Sc.
        
       Result-Graf
       This option is for viewing Gain, F/B and VSWR as a function of
       frequency.
       After selecting this option you will come to a menu where you can
       select which the reference frequency for VSWR .
       At this frequency VSWR will be 1:1.
       Press <ESC> to exit from the diagram.
        
       Current-Graf
       This function is for viewing the magnitude of the element current
       with the element with the greatest magnitude as reference.
       You can also compare the current from a different antenna with the
       same number of elements or from a different frequency.
        
       Current-Phase  (Graph)
       This function is for viewing the phase of the element current
       relative to the driver phase.
       The distance in degrees between the driver and the other elements 
       has been added to the actual current phase of the elements to
       give the real phase in the wave front.
       You can also compare the phase from a different antenna with the
       same number of elements or from a different frequency.



       Current
       Current shows the element currents and their phase position and
       magnitude.
       If you want to view the real element currents and their phase
       positions you can select this option.
       The currents are based on a supply voltage of 1 volt.
        
        


       Showing Noise Temperature (G/T)
       Shows Noise Temperature and G/T calculated with the OPTIONS 
       Noise Temperature (G/T). (See OPTIONS below for more information)


       OPTIONS MENU
        
       Dimension unit
       This option is for switching units between millimetres, inches and
       wavelengths.
       If you have entered data in one unit you can change to another
       unit with this option.
       The unit you have selected will be stored in Grafik.fil.
        
        
       Reflector type
       This option is for changing the reflector configuration.
       You can switch between single, double, triple, and triangular
       reflectors.
       The selected reflector configuration is stored in Grafik.fil.
        
        
       Driver type
       Here, you can select between straight or folded dipole.
       If you select folded dipole you will then be able to enter the
       length of the dipole and the spacing between the two dipole
       elements.
       If the calculation is to be correct it is important that the
       dipole be mounted symmetrically on the boom.
        
        
       Element pos
       This option allows you to select the form in which the element
       spacing is to be entered.
       If you select "Distance between" you will enter the spacing
       between two adjacent elements.
       If you select "x-values" you will enter the real position of the
       element on the boom with reference to the reflector which is "0".
        
       Change Colors
       This option allows you to select between three color settings:
       Color, Mono, and LCD.

       
        
       Wire Conductivity
       To be able to calculate how efficient an antenna is, it is
       important that the correct conductivity for the element material
       is entered.
       This option allows you to change the conductivity of the material
       you are using.
       The default value is 2.88E+07 which corresponds to 4104 and 6063-
       T6 aluminium.
       The <HELP> option will give you a table of the conductivity of
       different alloys.
        
       Ground/Stacking
       If the antenna height and stacking distance are zero, the Yagi 
       is modeled in free space. Set the height to a nonzero value to 
       model the Yagi over a perfectly-conducting groundplane.
       The antenna is always oriented for horizontal polarization
       over ground. The elevation angle is that at which the E-Plane 
       patterns are computed. To model a stacked pair of Yagis in free
       space, set the stacking distance to a nonzero value. This option
       takes mutal impedances into account when modelling stacked Yagis 
       or a single Yagi over ground. You can't use more than 44 element 
       in this option. If you want to stack more than two antennas, or 
       use more than 44 elements you must use the stacking option under
       RESULTS.



       Stacking
       Use this menu if you want to stack two or more antennas.
       The spacing in H- and E-plane respectively can be entered here.
       The first two data fields are for the number of antennas in the H-
       and E-plane respectively, while the two last data fields are for
       the spacing in each respective plane.
       This option cannot calculate the coupling between the antennas, as
       this would demand a very large memory and take too long when
       stacking large antennas.
       It is assumed that the coupling between antennas is negligible.
       When stacking in the E-plane (horizontally) this assumption is
       almost true even when the antennas are relatively close to each
       other. However, when stacking in the H-plane the spacing must be
       rather large to completely neglect the coupling between them. The
       shortest spacing that can be used is one wavelength.
       However, the coupling between antennas does not have too great an
       effect on the radiation pattern, so this will still show the real
       situation. The increase in gain though will always be 3 dB each
       time the number of antennas is doubled in respective plane, which
       is not always the case in reality.
       For this option it is the radiation pattern that is of greatest
       interest, not the gain.
        



       Noise Temperature (G/T)
       The effective noise temperature of antennas which "see" different 
       radiation sources with their pattern is a very important property,
       because it limits the achievable system temperature of the 
       complete reciving system. This property can be measured by indirect
       methods only. Noise temperature is dependent on the radiation pickup 
       of the main lobe in comparison to the pickup by the sidelobes. 
       For finite conductivity of the elements the resulting losses will 
       result in additional thermal noise.
       The derived measure of G/T-ratio is a very suitable quality feature 
       to compare different Yagi constructions and different stacking schemes
       for their value for EME-applications.Especially the latter criterion 
       has been subject of many, but mostly wrong, speculations of amateurs
       in the EME-community.

       The assumed elevation angle of the simulated Yagi  is 30 degrees. 
       The default temperature of sky is 15 K
       The default temperature of earth is 290 K

       Reference: DJ9BV "Effective Noise Temperature of 4-Yagi_Arrays for
       432 MHz EME",  Dubus magazin 4/1987

        
       YAGI ANLALYSIS FILE FORMAT
        
       The file format is changed since previous version.
       The extension is still .ANT and the file contain both input and
       output data.
       The first line is always ANTENNASPEC
       Here is an example of a 15el Yagi
        
       ANTENNASPEC
       15144              ' Antenna Name
       UNIT= mm           ' Dimension Unit can bee mm, Inch ,Wavel.
       144 MHz            ' The saving frequency ( E- and H-Pattern)
       143.5 MHz          ' Start frequency with swept antennas
       145.5 MHz          ' Stop frequency  with swept antennas
       REFLECTORTYPE= S   ' Reflector Type (S, D, T, R) see Options.
       Directors = 13     ' Number of directors
       Tapering=          ' If Tapering is chosen this line will be Yes
       Tap = 0            ' Number of Taper
       L1=278             ' L1 - L3 is distance between reflectors
       L2= 0              ' when more than one reflector is used
       L3= 0              ' Use <HELP> in Elementdata menu for more info.
       L4= 0
        
       Pos      ELLENGTH      RADIUS      ' These lines contain element
       0        1092          3          ' position, lengths and radii
       278      973           6
       501      963           3
       789      923           3
       1303     913           3
       1817     913           3
       2331     894           3
       2845     894           3
       3359     874           3
       3873     874           3
       4387     854           3
       4901     854           3
       5415     834           3
       5929     834           3
       6443     814           3
        
       COND= 2.88+07                  ' Wire Conductivity see Options
       BOOMCORR = 0                   ' Boom Corrections
       FOLDEDDIAMETER= 0              ' If folded dipol is used
       DRIVER=Singel                  ' Folded if folded dipol is used
       STEP=5                         ' Number of swept frequency
       FREQUENCYSTEP= .5 MHz          '
        
       ***OUTPUTDATA***
       DEG  E-PLANE                   ' Output data will contain
       1         0                    ' 360 lines with E- and H-Plane
       .                              ' pattern data and some other data
       .                              ' used with current computing
       .
        
        
        
        
       Frequency   Gain     F/B      Re imp   Im imp    3-dBE    3-dBH
       143.5        15.03    22.98   19.98    -3.45     16.62    17.94
       144          15.05    22.13   19.3     -.98      16.47    17.75
       144.5        15.05    21.38   18.43     1.5      16.32    17.58
       145          15.02    20.74   17.32     4.11     16.2     17.43
       145.5        14.95    20.14   15.95     6.99     16.1     17.32
        
       E-PLANE= 1              ' used with stacking antenna
       H-PLANE= 1              ' number of antenna stacked in each plane
       GAIN= 15.05 dBI         ' Antenna Gain with the saved pattern
       Efficency=98.7          ' Efficency in percent
        
       This new file format  can't be used with the older version of
       Yagi Analysis. So if you have an older version  you may take a
       backup of your old .ANT files.
       This version can read the older versions files but it saves them in
       the new file format.